Quiz Review
Pipelining, Hazards
+ Performance

---
1. Notate all dependencies (RAW, WAR, etc.) and control hazards in the following MIPS program “P”:
2.
(a) Diagram the pipeline schedule for the above MIPS code using the MIPS sequence IF-ID-EX-MEM-WB.
(b) Show all stalls and explain their purpose - why are they where you put them?
(c) Calculate the CPI for program P running on the MIPS pipeline, per your diagram.
   addi $t0,$t1,5
L: subi $t1,$t0,$t1
   beq $t0,$t1, L
   mult $t1,$t2

---
1. Notate all dependencies (RAW, WAR, etc.) and control hazards in the following MIPS program “P”:
No dependencies
WAR - on t1 with first line
RAW - on t0 with first line
RAR - on t1 with first line
   addi $t0,$t1,5
L: sub $t1,$t0,$t1
   beq $t0,$t1, L
   mult $t1,$t2
RAW - on t0 with first line
RAW - on t1 with 2nd line
RAR - on t1 with first line
RAR - on t1 with 2nd line
RAR - on t0 with 2nd line
?????

---
Resolving Data Hazards
Option 1: No forwarding
ID stage of instruction can not begin until WB stage is finished
Do not do this for this quiz!
Option 2: ALU - ALU Forwarding
Result of an instruction is forwarded from output of ALU to input of the next instruction's ALU
No stalls needed if instructions consecutive
Option 3: ALU - ID Forwarding
Result of instruction can only be forwarded to ID stage of next instruction.
1 Stall needed

---
Resolving Control Hazards
Option 1: Branch Prediction
Assume branch taken or not taken, then cancel incorrectly predicted instructions.
Do not do this for this quiz!
Option 2: Stall with no Forwarding
Stall until the branch instruction is entirely completed.
Do not do this for this quiz!
Option 3: Stall With ALU - IF Forwarding
Stall until the ALU stage is complete, then forward result of the branch to the next instruction.
Do this for this quiz!

---
No Forwarding at all.
01 02 03 04 05 06 07 08 09 10 11 12 13 14 15 16 17 18 19
 addi $t0,$t1,5
L:subi $t1,$t0,$t1
  beq $t0,$t1, L
  mult $t1,$t2
3 stalls were inserted before the subi insturction to wait for $t0 to be written back into the registers.
F
D
A
M
W
F
D
A
M
W
F
D
A
M
W
F
D
A
M
W

---
ALU - ALU Forwarding
01 02 03 04 05 06 07 08 09 10 11 12 13 14 15 16 17 18 19
 addi $t0,$t1,5
L:subi $t1,$t0,$t1
  beq $t0,$t1, L
  mult $t1,$t2
Don't forget to explain each stall and forward!
Example: "No stalls were inserted at subi because the ALU was able to forward $t0 from it's output to the ALU input for the next instruction."
F
D
A
M
W
F
D
A
M
W
F
D
A
M
W
F
D
A
M
W

---
ALU - ID Forwarding
01 02 03 04 05 06 07 08 09 10 11 12 13 14 15 16 17 18 19
 addi $t0,$t1,5
L:subi $t1,$t0,$t1
  beq $t0,$t1, L
  mult $t1,$t2
Don't forget to explain each stall and forward!
Example: "One stall was inserted for subi to wait for the ALU to forward $t0 to the ID of the next instruction."
F
D
A
M
W
F
D
A
M
W
F
D
A
M
W
F
D
A
M
W

---
ALU - ID Forwarding - CPI
01 02 03 04 05 06 07 08 09 10 11 12 13 14 15 16 17 18 19
 addi $t0,$t1,5
L:subi $t1,$t0,$t1
  beq $t0,$t1, L
  mult $t1,$t2
CPI
Assume the branch is not taken:
4 instructions, 11 clock cycles
CPI = 11/4
F
D
A
M
W
F
D
A
M
W
F
D
A
M
W
F
D
A
M
W